## Slide 1
EAHCP
Landa Lake Drought Management
EAHCP Conservation Measure Activities Through 2020s Drought
SCIENCE COMMITTEE IMPLEMENTATION MEETING
Meeting date · Location · Presenter
CLEAR WATER / VEGETATION MOSAIC / HABITAT STEWARDSHIP
01

## Slide 2
Edwards Aquifer Region Drought
04
ROLLING MONTHLY SPRINGFLOW
Current drought has reduced springflows at Comal to levels not experienced since the drought of record in the 1950s.
Daily mean springflow from USGS gage xxxx – Comal Springs, was aggregated to monthly means. Rolling averages represent the mean of consecutive monthly springflow values over the indicated 1- to 60-month periods.

## Slide 3
Edwards Aquifer Region Drought
04
ROLLING MONTHLY SPRINGFLOW
Current drought has reduced springflows at Comal to levels not experienced since the drought of record in the 1950s.
Points show the 50 lowest rolling-average springflow values for each averaging duration. Rolling periods overlap; for example, consecutive 12-month values may represent Jan–Dec 2024, Feb 2024–Jan 2025, and Mar 2024–Feb 2025. Colors identify periods ending in the 1950s and 2020s; all other periods are shown in black.

## Slide 4
Landa Lake Drought Management
CORE MESSAGE
04
PRESSURE POINTS
Lake wetted area
Lake level and culvert works
Dissolved oxygen
Temperature
Vegetation
Need a map here fo sure
TIME / REACH / VEGETATION TYPE
MEASURE
TAKEAWAY · Explain what changed, why it matters for habitat, and what the program is doing about it.

## Slide 5
Landa Lake Under Drought Conditions
LAKE LEVEL AND WETTED AREA
LBG-Guyton 20041
SR 1 and 2 stop flowing
LCRA well ~ 625 ft.
Comal flow ~ 130 cfs.
SR3 stops flowing when LCRA well ~ 621.5 ft. Comal flow ~ 50 cfs.
1LBG-Guyton Associates. 2004. Evaluation of Augmentation Methodologies in Support of In-Situ Refugia at Comal and San Marcos Springs, Texas. Prepared for the Edwards Aquifer Authority.
Make a graph of LCRA well 2025-1-1 to present

## Slide 6
Landa Lake Under Drought Conditions
LAKE LEVEL AND WETTED AREA
LBG-Guyton 20041
SR 1 and 2 stop flowing
LCRA well ~ 625 ft.
Comal flow ~ 130 cfs.
SR3 stops flowing when LCRA well ~ 621.5 ft. Comal flow ~ 50 cfs.
1LBG-Guyton Associates. 2004. Evaluation of Augmentation Methodologies in Support of In-Situ Refugia at Comal and San Marcos Springs, Texas. Prepared for the Edwards Aquifer Authority.
Make a graph of LCRA well 2025-1-1 to present
2025-2026 Observations
SR3 stops flowing when LCRA well ~ 620.25 ft. Comal flow ~ 50 cfs.

## Slide 7
Landa Lake Under Drought Conditions
LAKE LEVEL AND WETTED AREA
LBG-Guyton 20041
SR 1 and 2 stop flowing
LCRA well ~ 625 ft.
Comal flow ~ 130 cfs.
SR3 stops flowing when LCRA well ~ 621.5 ft. Comal flow ~ 50 cfs.
Picture on left is Spring Run 3 facing downstream from walking bridge on May 21, 2025 (Total Comal discharge 49 cfs). Picture on the right is WQ monitoring equipment attached to same walking bridge on April 1, 2026 (Total Comal discharge 53 cfs).
2025-2026 Observations
SR3 stops flowing when LCRA well ~ 620.25 ft. Comal flow ~ 50 cfs.
Add one more sr3

## Slide 8
Landa Lake Under Drought Conditions
CORE MESSAGE
04
LANDA LAKE HYDROLOGY
Surface discharge is measured at four spring runs and four lake cross sections to estimate springflow contributions from different areas of the lake.
TAKEAWAY · Explain what changed, why it matters for habitat, and what the program is doing about it.
Make a graph of spring orifices

## Slide 9
Landa Lake Under Drought Conditions
CORE MESSAGE
04
LANDA LAKE HYDROLOGY
Surface discharge is measured at four spring runs and four lake cross sections to estimate springflow contributions from different areas of the lake.
TAKEAWAY · Explain what changed, why it matters for habitat, and what the program is doing about it.

## Slide 10
Landa Lake Under Drought Conditions
CORE MESSAGE
04
LANDA LAKE FLOW SPLIT
TAKEAWAY · Explain what changed, why it matters for habitat, and what the program is doing about it.
Bring it back home with one more graph
Showing the viewer where that water is coming from

## Slide 11
Landa Lake Under Drought Conditions
CORE MESSAGE
04
LANDA LAKE FLOW SPLIT
Describe how water is distributed among lake at this level
TAKEAWAY · Explain what changed, why it matters for habitat, and what the program is doing about it.
Perhaps a few pictures here, visual tour

## Slide 12
Landa Lake Flow Split Management
LAKE CONTEXT
05
FLOW SPLIT MANAGEMENT
EAHCP § 5.2.1
Flow split management in the Old and New Channel
Old Channel Protection
Flow split management is intended to complement the ecological restoration of aquatic vegetation in the Old Channel, by reducing long-duration high flows and allowing for more seasonal variability to be maintained, mimicking a more natural flow pattern.
Culvert Management
Flow manipulations are managed by City of New Braunfels according to season and total system discharge.
Table 5-3 EAHCP Flow split management for Old and New channels

## Slide 13
Landa Lake Flow Split
CORE MESSAGE
04
FLOW SPLIT
Priority will be given to achieving target flow rates in the Old Channel and, secondly, to flow rates in the New Channel.
City of New Braunfels staff will monitor streamflow conditions via USGS streamflow gages and operate the flow-control gates between Landa Lake and the Old Channel to achieve flow targets.
Maintenance activities associated with the flow-control gates will be conducted as needed to ensure continued operability.
TAKEAWAY · Explain what changed, why it matters for habitat, and what the program is doing about it.

## Slide 14
Landa Lake Flow Split
CORE MESSAGE
04
FLOW SPLIT
Priority will be given to achieving target flow rates in the Old Channel and, secondly, to flow rates in the New Channel.
City of New Braunfels staff will monitor streamflow conditions via USGS streamflow gages and operate the flow-control gates between Landa Lake and the Old Channel to achieve flow targets.
Maintenance activities associated with the flow-control gates will be conducted as needed to ensure continued operability.
TAKEAWAY · Explain what changed, why it matters for habitat, and what the program is doing about it.

## Slide 15
Landa Lake Flow Split
CORE MESSAGE
04
FLOW SPLIT
TAKEAWAY · Explain what changed, why it matters for habitat, and what the program is doing about it.
Priority will be given to achieving target flow rates in the Old Channel and, secondly, to flow rates in the New Channel.
City of New Braunfels staff will monitor streamflow conditions via USGS streamflow gages and operate the flow-control gates between Landa Lake and the Old Channel to achieve flow targets.
Maintenance activities associated with the flow-control gates will be conducted as needed to ensure continued operability.

## Slide 16
Landa Lake Vegetation Management
LAKE CONTEXT
05
MAP / PHOTO / SITE FIGURE
Replace with Landa Lake reach map, drone image, transect photo, or monitoring station map.
SUBMERGED AQUATIC VEGETATION
1
EAHCP § 5.2.2
Native Aquatic Vegetation Restoration and Maintenance
2
Provide Beneficial Habitat
To minimize and mitigate the impacts of incidental take from low-flow events by providing better habitat conditions for the ecological community.
3
Restoration Goals
Restoration activities occur in Long-term Biological Goal Reaches designated by the EAHCP as well as supportive Restoration Reaches which provide further habitat enhancement objectives.

## Slide 17
Landa Lake Vegetation Maintenance
CORE MESSAGE
04
SUBMERGED AQUATIC VEGETATION
Restoration activities have been moderated by Condition M of the permit with flows < 130 cfs.
Currently, only Ludwigia and Cabomba are propagated and planted.
~ 3500 plants were planted across six restoration plot areas (~ 750 m2)
TAKEAWAY · Explain what changed, why it matters for habitat, and what the program is doing about it.
Perhaps a few pictures here, visual tour

## Slide 18
Landa Lake Vegetation Maintenance
CORE MESSAGE
04
SUBMERGED AQUATIC VEGETATION
Restoration activities have been moderated by Condition M of the permit with flows < 130 cfs.
Currently, only Ludwigia and Cabomba are propagated and planted.
~ 3500 plants were planted across six restoration plot areas (~ 750 m2)
TAKEAWAY · Explain what changed, why it matters for habitat, and what the program is doing about it.
Perhaps a few pictures here, visual tour

## Slide 19
Landa Lake Riparian Management
Use this layout for a map/photo paired with a compact site-specific interpretation.
LAKE CONTEXT
05
MAP / PHOTO / SITE FIGURE
Replace with Landa Lake reach map, drone image, transect photo, or monitoring station map.
WHAT THE FIGURE SHOWS
1
Habitat setting
Location-specific finding: reach, shoreline condition, vegetation patch, or flow path.
2
Interpretation context
Why season, springflow, clarity, or survey design matters for this result.
3
Point requiring attention
Use coral only for a stressor, threshold, management issue, or discussion item.

## Slide 20
Landa Lake Water Quality
Use this layout for a map/photo paired with a compact site-specific interpretation.
LAKE CONTEXT
05
MAP / PHOTO / SITE FIGURE
Replace with Landa Lake reach map, drone image, transect photo, or monitoring station map.
WHAT THE FIGURE SHOWS
1
Habitat setting
Location-specific finding: reach, shoreline condition, vegetation patch, or flow path.
2
Interpretation context
Why season, springflow, clarity, or survey design matters for this result.
3
Point requiring attention
Use coral only for a stressor, threshold, management issue, or discussion item.

## Slide 21
Got to have something about the species
A simple pathway clarifies triggers, responsibilities, and intended habitat outcomes.
IMPLEMENTATION PATHWAY
08
OBSERVE
01
Vegetation + habitat signal
Mapped vegetation, photo points, field notes, water clarity, springflow context.
INTERPRET
02
Ecological meaning
Separate normal seasonal movement from persistent habitat change.
MANAGE
03
Implementation action
Coordinate mowing, recreation management, restoration, or monitoring adjustment.
EVALUATE
04
Outcome and learning
Assess vegetation response, habitat quality, and what to change next cycle.
KEY QUESTION · Is each handoff clear, documented, and supported by the right monitoring evidence?

## Slide 22
Management Tools Available
MONITORING STATUS
09
COMPONENT
PURPOSE IN LANDA LAKE
CURRENT STATUS
NEXT USE
Vegetation Management
Describe the mechanism and ecological value of the survey product.
ON TRACK
Briefing
Flow Split Management
Describe what the field observation adds to the mapped data.
WATCH
QA/QC
Riparian Management
Describe the interpretive value for clarity, flow, or habitat condition.
ACTIVE
Context
Monitoring
Describe how implementation actions are documented and connected to outcomes.
UPDATE
Decision
DISCUSSION PROMPT · Which monitoring components are ready for interpretation, and which need more field context?

## Slide 23
How to use this deck
Keep this slide as a reference, then remove it from the final briefing.
TEMPLATE DESIGN SYSTEM
02
PALETTE
LAKE DEEP
LAKE
SHALLOW
AQUATIC
CYPRESS
LIMESTONE
GOLD
CORAL
TYPE
Aptos Display
Scientific headings; compact enough for maps, monitoring figures, and annotated tables.
SLIDE RULE
One Landa Lake message per slide.
Use the headline to state the ecological or implementation finding—not merely name the dataset.
FIGURE RULE
Direct attention with one accent.
Most data stay lake blue, aquatic green, or gray. Use coral only for thresholds, stressors, exceptions, or decisions.
TEMPLATE GUIDANCE

## Slide 24
01
Landa Lake
Habitat
Section subtitle or implementation question
Use section dividers to reset the room and frame the lake-specific question that the next slides answer.
SECTION DIVIDER
03

## Slide 25
Lake context sets the interpretation for every result
Use this layout for a map/photo paired with a compact site-specific interpretation.
LAKE CONTEXT
05
MAP / PHOTO / SITE FIGURE
Replace with Landa Lake reach map, drone image, transect photo, or monitoring station map.
WHAT THE FIGURE SHOWS
1
Habitat setting
Location-specific finding: reach, shoreline condition, vegetation patch, or flow path.
2
Interpretation context
Why season, springflow, clarity, or survey design matters for this result.
3
Point requiring attention
Use coral only for a stressor, threshold, management issue, or discussion item.

## Slide 26
Vegetation condition should connect trend, composition, and habitat value
Use this for annual area, percent cover, or mapped vegetation classes.
VEGETATION MONITORING
06
PRIMARY VEGETATION FIGURE
Line, stacked area, or faceted figure. Keep the legend compact and put the finding in the headline.
CONDITION
Replace with current-year status, direction of change, or monitoring category.
HABITAT LINK
State how the vegetation condition supports habitat, refugia, or covered-species needs.

## Slide 27
Major vegetation types tell the habitat story better than total area alone
Use this layout when composition is the key message.
VEGETATION COMPOSITION
07
A · COMPOSITION FIGURE
Example: stacked area by dominant vegetation type, grouped bars by survey date, or mosaic summary.
B · KEY COMPARISON
Example: specific species/class, pre/post management interval, or reach comparison.
COMPARE

## Slide 28
Show how lake evidence becomes implementation
A simple pathway clarifies triggers, responsibilities, and intended habitat outcomes.
IMPLEMENTATION PATHWAY
08
OBSERVE
01
Vegetation + habitat signal
Mapped vegetation, photo points, field notes, water clarity, springflow context.
INTERPRET
02
Ecological meaning
Separate normal seasonal movement from persistent habitat change.
MANAGE
03
Implementation action
Coordinate mowing, recreation management, restoration, or monitoring adjustment.
EVALUATE
04
Outcome and learning
Assess vegetation response, habitat quality, and what to change next cycle.
KEY QUESTION · Is each handoff clear, documented, and supported by the right monitoring evidence?

## Slide 29
Monitoring is easiest to review by purpose and status
Use this table for vegetation mapping, photo points, water quality, recreation observations, or targeted surveys.
MONITORING STATUS
09
COMPONENT
PURPOSE IN LANDA LAKE
CURRENT STATUS
NEXT USE
Vegetation mapping
Describe the mechanism and ecological value of the survey product.
ON TRACK
Briefing
Photo points / field notes
Describe what the field observation adds to the mapped data.
WATCH
QA/QC
Water-quality context
Describe the interpretive value for clarity, flow, or habitat condition.
ACTIVE
Context
Management action record
Describe how implementation actions are documented and connected to outcomes.
UPDATE
Decision
DISCUSSION PROMPT · Which monitoring components are ready for interpretation, and which need more field context?

## Slide 30
Pair lake condition with program response
Use aligned figures when the comparison—not either figure alone—is the message.
CONDITION + RESPONSE
10
A · LAKE CONDITION
Examples: vegetation extent, percent cover, mapped habitat, water clarity, or springflow context.
B · PROGRAM RESPONSE
Examples: maintenance, restoration, recreation management, monitoring adjustment, or adaptive response.
COMPARE

## Slide 31
What should the committee discuss?
Use this slide to convert information into focused scientific dialogue.
DISCUSSION / DECISION
11
01
Is the evidence sufficient?
Identify gaps in mapping, field interpretation, or communication.
02
Is implementation performing as intended?
Separate operational execution from ecological outcome.
03
What should change before the next cycle?
Name a specific analysis, action, or decision owner.
COMMITTEE
DISCUSSION

## Slide 32
Looking forward: protect the next lake monitoring cycle
Organize the close around near-term commitments—not a generic summary.
NEXT STEPS
12
NOW
Before the next operational milestone
Confirm current status
Close immediate data gaps
Document decisions
NEXT CYCLE
Before the next committee meeting
Complete targeted analyses
Refine habitat indicators
Track agreed actions
LONGER TERM
Program learning agenda
Improve integration across measures
Evaluate performance over time
Identify adaptive changes
CLOSE WITH OWNERSHIP · Who will do what, by when, and what evidence will show completion?

## Slide 33
EAHCP · LANDA LAKE HABITAT
Questions and
discussion
Appendix slides may follow using the same figure, map, monitoring, and status layouts.
PRESENTER · TITLE · CONTACT
Edwards Aquifer Habitat Conservation Plan
13